## Slide 1
RESEARCH PROPOSAL
Binary-Gated PQCache
A retrofit compressed sparse-KV algorithm that makes K directly searchable, uses PQ for reranking, and only becomes a chip target after CPU/GPU evidence.
1. Algorithm
CPU implementation proves quality, bytes saved, and selector recall before kernel work.
2. Systems
GPU prototype exposes bit-packing, top-k, compaction, and sparse page-fetch bottlenecks.
3. Hardware
Custom datapath accelerates the measured bottleneck primitives, not one fixed paper design.
May 2, 2026
Proposal synthesized from PQCache, self-indexing/hash KV, completion fallback, and chip-oriented discussion.
1

## Slide 2
PROPOSAL
The research bet is not PQCache alone; it is a searchable compressed-KV substrate.
Treat PQCache as a strong component inside a more general selector-plus-memory design.
No benchmark claims here; this slide defines the proposal.
2
Thesis
Binary/hash codes should do recall; PQ should repair ranking; quantized V pages should carry the bandwidth win.
Why now
Long decode turns KV cache into the dominant memory object; retrofit methods fit deployed dense/GQA/MLA models.
Main question
Can selector metadata also be the compressed K representation without losing attention quality?
Go/no-go
Proceed toward hardware only if CPU quality holds and GPU bottlenecks map to compact custom primitives.

## Slide 3
BOTTLENECK
Long decode is a memory-system problem before it is an attention-math problem.
The algorithm should be judged by selected bytes and recovered quality, not by asymptotic sparsity alone.
Variables are evaluation targets, not reported results.
3
Dense step
read all K + read all V + softmax over N
Hybrid step
K sidecar scan
M candidates
K final rows
completion
BYTES SAVED
measure
K sidecar + sparse V pages vs dense KV
QUALITY LOSS
bound
top-k recall, logit error, KL, task score
IRREGULARITY COST
expose
top-k, gather, compaction, bit ops on GPU
HARDWARE CASE
justify
only if custom primitives beat GPU pain

## Slide 4
ALGORITHM
Binary-gated PQCache turns selection into a hierarchy, not one approximate scan.
The binary stage maximizes cheap recall; the PQ stage spends accuracy only on a small candidate set.
M is the coarse candidate budget; K is the final sparse attention budget.
4
q
current query
binary code
sign/hash encoder
bit match
XNOR + popcount
top M
candidate IDs/pages
PQ rerank
LUT score
top K
final rows
V pages
int4/int8 fetch
output
softmax + fallback
Coarse stage
Full-cache scan is allowed only because each token is a few packed bits.
Fine stage
PQ LUT scores are paid only for M candidates, not every cached key.
Final stage
Sparse V fetch is the expensive read; it must be page-aware and coalesced.

## Slide 5
MEMORY LAYOUT
The selector metadata should also be the compressed K memory.
Do not store a compressed key and then build a separate index if the compressed key can be searched directly.
Sidecar fields are illustrative; CPU ablations should decide which survive.
5
Object
Stored fields
Used during decode
Reason
K sidecar
b_i, pq_i, norm_i, bank_id
every step
search and approximate score without FP16 K read
K escape tier
int8/full K for outliers
selected candidates only
protect rare keys that PQ/hash represents poorly
V page
quantized V, scales, token map
top K fetch
dominant bandwidth object after selection
Summary page
completion numerator/denominator state
fallback path
recover diffuse attention mass without fetching all V
Per token:
b_i bits
PQ code
norm
flags
Small enough to scan; expressive enough to rerank.

## Slide 6
DECODE FLOW
Decode uses bit matching for recall and PQ LUTs for ranking fidelity.
The CPU prototype should expose every intermediate set so recall losses are measurable.
The final exact-ish step can use reconstructed K_hat or quantized K only for candidates.
6
Query path
K sidecar
Sparse memory
encode q
b_q and PQ LUTs
coarse scan
popcount over b_i
candidate set
top M IDs/pages
fine rerank
sum LUT[pq_i] + norm
fetch top K
V pages + optional K
attention
softmax over selected rows
completion
add missing mass summary

## Slide 7
K RECONSTRUCTION
K reconstruction should be residual and versioned, not a growing centroid count.
Long decode may widen the key distribution, but changing centroid count dynamically makes old codes hard to interpret.
Recommendation: fixed hardware shape, multiple codebook banks, residual PQ, and outlier escape.
7
Avoid
growing C over time
forces recoding or version chaos
Accept
page/epoch codebook banks
old pages keep bank_id; LUTs are generated per active bank
Prefer
binary coarse + residual PQ
k_hat = center(b_i) + residual_PQ(p_i)
Proposed K_hat path
b_i selects a coarse region; pq_i stores residual code; norm_i restores logit scale; outlier flag routes to higher precision.

## Slide 8
V AND FALLBACK
V compression is separate, but selected pages and completion summaries share the same scheduler.
Binary/PQ metadata can reconstruct K_hat; values still need their own low-bit storage and a missing-mass path.
Completion is a quality guardrail, not a replacement for selecting important tokens.
8
Selected path
top K token IDs -> quantized V page fetch -> local dequant -> exact selected contribution
Missing path
unfetched pages -> small summary state -> approximate numerator/denominator correction
+
output = (selected numerator + completion numerator) / (selected denominator + completion denominator)
Design implication: the memory controller must fetch sparse V pages and stream summary pages with predictable latency.

## Slide 9
CPU PHASE
CPU work should answer whether the algorithm is accurate enough before kernel work begins.
Start with an exact, inspectable harness; do not optimize before selector failure modes are visible.
CPU target: correctness and bytes/quality accounting, not serving throughput.
9
Build item
What it computes
Gate
Trace collector
Q,K,V and exact attention from target models
reproducible tokens, heads, layers, tasks
Selector simulator
binary recall, PQ rerank, optional K_hat logits
recall@M/K and logit error per head
Compression accounting
sidecar bytes, V bytes, summary bytes
capacity and bandwidth estimates
Quality harness
perplexity, needle, code, reasoning, long-output drift
no hidden task cliff at target budgets
Kill criterion
If candidate recall must be so large that V fetch dominates again, the algorithm is not a chip target.

## Slide 10
ABLATIONS
The ablation grid should isolate which metadata actually buys quality.
Every extra bit in the sidecar must justify itself against attention quality and fetch reduction.
Rows become implementation flags in the CPU harness.
10
Ablation
Knob
Quality readout
Memory readout
Expected decision
Binary bits
64 / 128 / 256
candidate recall
sidecar scan bytes
minimum viable m
PQ shape
M subspaces, C centroids
rerank error
LUT and code bytes
residual or plain PQ
Codebook bank
global / page / epoch
drift by token age
LUT setup pressure
fixed banks, not growing C
Outlier tier
none / int8 / full K
rare-key failures
escape bytes
keep only if tails matter
Completion
off / page / segment
softmax KL, long-output drift
summary bytes
fallback threshold

## Slide 11
GPU PHASE
GPU work should benchmark the ugly parts, not just count bytes saved.
The GPU prototype is valuable because it reveals which theoretical savings survive real kernels.
Use dense attention and strong sparse/KV baselines; report both quality and wall-clock decode.
11
Prototype path
PyTorch reference -> Triton/CUDA kernels -> serving integration slice
Measure
tokens/s, latency/token, HBM bytes, occupancy, gather efficiency, kernel launch count
Compare
dense/GQA baseline, KV quant baseline, PQCache-like selector, hash-only selector
GPU success is not only speedup.
It is a bottleneck map: which stages remain slow because GPUs dislike bit-packed scans, top-k, compaction, and sparse gathers.

## Slide 12
BOTTLENECKS
GPU bottlenecks become the hardware feature list.
If a stage is fast on GPU, do not spend silicon on it; if it is slow but quality-critical, it becomes a primitive.
This slide defines what the GPU experiment should report.
12
GPU pain
Why it happens
Custom primitive
Decision
1-bit scan
packed bits and popcount are not the standard attention path
bit-sliced SRAM + popcount lanes
keep if M recall works
top-M/top-K
selection and compaction are irregular
streaming threshold/top-k network
budget by latency
PQ LUT rerank
small random LUT access and reductions
local centroid SRAM + fixed reduction tree
share across heads
V page gather
selected IDs are not naturally coalesced
page scheduler + reorder buffer
make pages the unit
completion
summary path competes with selected path
parallel summary accumulator
gate by entropy

## Slide 13
HARDWARE TARGET
Custom hardware should specialize primitives, not freeze one paper's selector.
The candidate engine should support a small template: binary recall, PQ refinement, optional exact-ish rerank, sparse V fetch.
Hardware sketch assumes an external HBM/DRAM KV store plus on-chip sidecar/codebook SRAM.
13
Query encoder
sign/hash + PQ LUTs
>
Sidecar SRAM
b_i, pq_i, norm, flags
>
Popcount lanes
coarse scores
>
Top-M buffer
candidate IDs
>
PQ rerank
LUT reduction
>
Page engine
fetch/dequant V
Completion accumulator
summary numerator/denominator in parallel with selected rows

## Slide 14
HARDWARE MODEL
The hardware model must translate quality budgets into bytes, SRAM, and energy.
Do not claim a chip win from algorithmic sparsity alone; model the memory hierarchy and selector datapath explicitly.
Outputs should be comparable against a GPU measured bottleneck profile.
14
Input
Algorithm source
Hardware parameter
Output metric
m bits/token
binary recall ablation
sidecar SRAM/HBM traffic
scan energy/token
PQ bytes/token
rerank error ablation
codebook SRAM + LUT bandwidth
rerank energy/token
K and M budgets
quality-vs-fetch curve
top-k buffer size
latency/token
V page size
sparse fetch locality
page scheduler and dequant lanes
HBM transactions/token
completion summary
diffuse-head failure rate
summary SRAM and accumulator
quality recovery per byte

## Slide 15
PLAN
The project should have explicit go/no-go gates before tapeout effort.
The fastest path is to disprove weak variants early and keep only primitives with measured value.
Timeline is a research plan, not a promise about calendar duration.
15
0-2 wk
Trace + exact baseline
collect Q/K/V, dense attention, task harness
>
3-6 wk
CPU selector study
binary/PQ/residual/completion ablations
>
7-10 wk
GPU prototype
Triton/CUDA kernels, benchmark and counters
>
11-13 wk
Hardware model
primitive sizing, bytes, energy, scheduler model
>
14-16 wk
Proposal freeze
choose chip-facing algorithm or pivot
Main gate
Do not move to hardware unless the CPU quality curve and GPU bottleneck profile both point to the same small set of primitives.

## Slide 16
CONTRIBUTION
The expected contribution is an algorithm, benchmark, and chip co-design target.
The work should be publishable even if the final answer is that a narrower variant is the right hardware target.
Risks are useful because they define the measurement plan.
16
Area
Contribution
Main risk
Algorithm
Binary-gated residual PQCache with completion-aware fallback
binary recall fails on important heads
Evaluation
CPU/GPU harness that reports quality, bytes, and irregularity cost together
benchmark too model/task-specific
Systems
GPU bottleneck profile for compressed sparse KV selectors
savings erased by compaction and gather overhead
Hardware
datapath template for searchable compressed K and sparse quantized V
primitive set too broad or not enough reuse
Strong outcome: a selector/memory algorithm that GPUs struggle to exploit but custom hardware can make regular.

## Slide 17
SOURCES
Primary references for the proposal.
The proposed hybrid is a synthesis; these sources motivate the components, not a single reported system.
URLs are plain text for easy copy/paste.
17
PQCache
https://arxiv.org/abs/2407.12820
Self-Indexing KVCache
https://arxiv.org/abs/2603.14224
DASH-KV
https://arxiv.org/abs/2604.19351
Top-K + Completion
https://arxiv.org/abs/2604.05438
ShadowKV
https://arxiv.org/abs/2410.21465
ParisKV
https://arxiv.org/abs/2602.07721
RetrievalAttention
https://arxiv.org/abs/2409.10516
RocketKV
https://arxiv.org/abs/2502.14051
SWAN
https://arxiv.org/abs/2511.18936